## Slide 1: Electrolytic method of hydrogen production.
The simplest way: [1][2]
There is no catalyst involved to aid the rate of reaction.
A common electrolyte for cells like this is KOH.
Reduction occurs at the cathode, where 2H+ + 2e- -> H2
Oxidation occurs at the anode, where 2H2O -> 4H+ + 4e- + O2
In the standard state, this reaction has E0cell = -1.228V.
In practice, at higher O2 partial pressure or higher pH this reaction can be even more energetically expensive.
While this process is valuable, it can be improved on.
Improvements on the uncatalysed method can be made through various optimizations. We can use a catalyst, control the pH and O2 and H2 partial pressure inside the reaction as well as the type of electrodes used.
Catalysts which are suitable for this kind of reaction generally help the oxidation reaction, as the evolution of O2 is generally slower than H2.[2] Amorphic metal catalysts such as NiFe can have high performance in these applications.
Why produce hydrogen in the first place?[1]
Hydrogen when used in a fuel cell is an extremely clean and efficient way of storing energy.
Water as a source of fuel is a very good idea, it is a naturally abundant feedstock.
PEM fuel cells operate by the following route:[1][2]
H2 -> 2H+ +2e- at the anode.
These protons are in solution and pass through the membrane to the cathode.
O2 + 4H+ + 4e- -> 2H2O
The movement of electrons generates an electric current.
[1] P. Hoffmann and B. Dorgan, in Why Hydrogen? The Grand Picture, MIT Press, 2012, pp. 1–17.
[2] M. D. Merrill, Thesis, 2006, 1–86.
By Ellis Lunnon
Fig. 1 – SEM image at 5 levels of the NiFe catalyst surface.
Fig. 2 – Schematic diagram of a PEM fuel cell